## Slide 1: Forces and Resultant Force

## Slide 2: Force: A Vector
Forces are specified using two quantities: the magnitude and the direction of the force.
In polar form, F = erFr + eθF θ
F = magnitude (Newtons, N or lbs)
θ = direction (degrees or rad)
In rectangular form F = iFx + jFy = Fx
Fy
F: magnitude
θ: direction
x
y
^
^
er,Fr
eθ,F θ
i,Fx
j,Fy

## Slide 3: Quick Review of Basic Trig
α
x
y
h
sin(α) = y/h
cos(α) = x/h
tan(α) = y/x
x2 + y2 = h2

## Slide 4: Force Conversions
Polar to Rectangular:
Fx = Fcos(θ) Force in x-direction
Fy = Fsin(θ) Force in y-direction
Rectangular to Polar:
F = √Fx2 + Fy2
θ = tan-1(Fy/Fx)
F
θ
x
y
Fx
Fy

## Slide 5: Computing Resultant Force
Numerical Solution:
Resolve each force into an x and y component (rectangular).
Sum all of the x components and all of the y components to get the x and y component of the resultant force.
Calculate the magnitude and direction of the resultant force from the x and y components.
F1 = 100∠50o N
F2 = 50∠-30o N
F3 = 30∠130o N

## Slide 6: Computing Resultant Force
F1x = 100*cosd(50) = 64.3 F2x = 50*cosd(-30) = 43.3 F3x = 30*cosd(130) = -19.3
F1y = 100*sind(50) = 76.6 F2y = 50*sind(-30) = -25 F3y = 30*sind(130) = 23
FRx = F1x + F2x + F3x = 64.3 + 43.3 + -19.3 = 88.3 N
FRy = F1y + F2y + F3y = 76.6 – 25 + 23 = 74.6 N
F1 = 100∠50o N
F2 = 50∠-30o N
F3 = 30∠130o N
64.3
76.6
43.3
-25.0
-19.3
23.0

## Slide 7: Computing Resultant Force
Magnitude = sqrt(88.32 + 74.62) = 115.6
Direction = atand(Fy/Fx) = 40.2o
Note: If Fx is negative, add 180o to the direction calculated using
MATLAB® or calculator.
F1 = 100∠50o
F2 = 50∠-30o N
F3 = 30∠130o N
F = 115∠40.2o N
74.6
88.3